## Slide 1: Warm-Up – 3/22 – 10 minutes
Utilizing your notes and past knowledge answer the following questions:
What instrument is required to be installed by 14CFR Part 91 during VFR and IFR flight operations?
What are the letters and numbers marked on the magnetic compass and how many degrees apart are they?
The long and short graduation marks are spaced how many degrees apart on a magnetic compass?
Describe what conditions may cause compass deviation.
What instrument/gauge provides the pilot with useful information about temperature lapse rate with altitude change?

## Slide 2: Questions / Comments

## Slide 3: Warm-Up – 3/22 – 10 minutes
Utilizing your notes and past knowledge answer the following questions:
What instrument is required to be installed by 14CFR Part 91 during VFR and IFR flight operations?
What are the letters and numbers marked on the magnetic compass and how many degrees apart are they?
The long and short graduation marks are spaced how many degrees apart on a magnetic compass?
Describe what conditions may cause compass deviation.
What instrument/gauge provides the pilot with useful information about temperature lapse rate with altitude change.

## Slide 4: Magnetic Compass
One of the oldest and simplest instruments for indicating direction is the magnetic compass.
It is also one of the basic instruments required by Title 14 of the Code of Federal Regulations (14 CFR) part 91 for both VFR and IFR flight.

## Slide 5: Warm-Up – 3/22 – 10 minutes
Utilizing your notes and past knowledge answer the following questions:
What instrument is required to be installed by 14CFR Part 91 during VFR and IFR flight operations?
What are the letters and numbers marked on the magnetic compass and how many degrees apart are they?
The long and short graduation marks are spaced how many degrees apart on a magnetic compass?
Describe what conditions may cause compass deviation.
What instrument/gauge provides the pilot with useful information about temperature lapse rate with altitude change.

## Slide 6: Magnetic Compass
An aircraft magnetic compass is marked with letters representing the cardinal directions, north, east, south, and west, and a number for each 30° between these letters.
The final “0” is omitted from these directions.
For example, 3 = 30°, 6 = 60°, and 33 = 330°.

## Slide 7: Warm-Up – 3/22 – 10 minutes
Utilizing your notes and past knowledge answer the following questions:
What instrument is required to be installed by 14CFR Part 91 during VFR and IFR flight operations?
What are the letters and numbers marked on the magnetic compass and how many degrees apart are they?
The long and short graduation marks are spaced how many degrees apart on a magnetic compass?
Describe what conditions may cause compass deviation.
What instrument/gauge provides the pilot with useful information about temperature lapse rate with altitude change.

## Slide 8: Magnetic Compass
There are long and short graduation marks between the letters and numbers.
Each long mark representing 10° and each short mark representing 5°.

## Slide 9: Warm-Up – 3/22 – 10 minutes
Utilizing your notes and past knowledge answer the following questions:
What instrument is required to be installed by 14CFR Part 91 during VFR and IFR flight operations?
What are the letters and numbers marked on the magnetic compass and how many degrees apart are they?
The long and short graduation marks are spaced how many degrees apart on a magnetic compass?
Describe what conditions may cause compass deviation.
What instrument/gauge provides the pilot with useful information about temperature lapse rate with altitude change.

## Slide 10: Magnetic Compass Deviation
Magnetic fields in an aircraft caused by electrical current flowing in the structure
Nearby wiring or any magnetized part of the structure
Conflict with the Earth’s magnetic field and cause a compass error called deviation.

## Slide 11: Warm-Up – 3/22 – 10 minutes
Utilizing your notes and past knowledge answer the following questions:
What instrument is required to be installed by 14CFR Part 91 during VFR and IFR flight operations?
What are the letters and numbers marked on the magnetic compass and how many degrees apart are they?
The long and short graduation marks are spaced how many degrees apart on a magnetic compass?
Describe what conditions may cause compass deviation.
What instrument/gauge provides the pilot with useful information about temperature lapse rate with altitude change?

## Slide 12: Outside Air Temperature (OAT) Gauge
OAT gauges are calibrated in degrees °C, °F, or both.
An accurate air temperature provides the pilot with useful information about temperature lapse rate with altitude change.

## Slide 13: Questions / Comments

## Slide 14: THIS DAY IN AVIATION
March 22
1915 — The term “Naval Aviator” is adapted for United States Navy officer pilots to replace the identification “Navy Air Pilot“ in official terminology.
This term is still in use today.

## Slide 15: THIS DAY IN AVIATION
March 22
1966 — 20 high schools are selected to start the new Junior ROTC program.

## Slide 16: THIS DAY IN AVIATION
March 22
1989 — The first and only Antonov An-225 built establishes 106 new Federal Aeronautique Internationale (FAI) world records in several classes, most important of which is a speed of 813.09 km/h (505.2 mph) carrying a payload in the 70-155 metric ton (154,320-341,710 lb.) class around a closed circuit of 2,000 km (1,243 miles).

## Slide 17: Questions / Comments

## Slide 18
Sunday | Monday | Tuesday | Wednesday | Thursday | Friday | Saturday
25 | 26 Chapter 6 Flight Systems Powerplants | 27 Chapter 6 Flight Systems Propellers | 28 Chapter 6 Flight Systems Induction Carb Systems | 1 Chapter 6 Flight Systems Carb Icing and Heating | 2 Flight Line Friday QUIZ | 3
4 | 5 Chapter 6 Ignition Systems | 6 Chapter 6 Oil Systems | 7 Chapter 6 Fuel Systems | 8 Chapter 6 Electrical Systems | 9 Mighty 8th Museum | 10
11 | 12 Chapter 7 Flight Instruments | 13 Chapter 7 Flight Instruments Altimeter | 14 Chapter 7 Flight Instruments Vertical Speed Indicator | 15 Chapter 7 Flight Instruments Airspeed Indicator | 16 Flight Line Friday QUIZ | 17
18 | 19 Chapter 7 Flight Instruments Gyro Systems | 20 Chapter 7 Flight Instruments Magnetic Compass | 21 Chapter 7 Flight Instruments Review and Test | 22 Chapter 8 Flight Manuals | 23 Chapter 8 Flight Manuals Review and Test | 24
February / March 2018

## Slide 19: Questions / Comments

## Slide 20: 2nd Quarter Requirements (9 weeks – May 18)
All students will complete the following:
  Take notes - All in class quizzes and tests
  Private Pilot Syllabus
    Lessons 1 – 5 (Taxiing through Air Traffic Control)
    Must pass written with 80%
    Successfully complete 3 times on small sim
    Successfully complete 1 time on Main sim
  Complete ERAU Aviation 101
    3 quizzes and 1 test
  Student will receive zero points for all incomplete work – NO make-up / extra credit
NOTE: All unfinished Student Pilot and ERAU must be complete prior to starting Private Pilot and last 3 quizzes and test for ERAU.

## Slide 21: Questions / Comments

## Slide 22: AVIATION ACES
1B
Pilots (A – 90 & above)
Abercrombie
Potato
Blackbird
Mike
Frenchie
Brad
Bo
1B
Co-Pilots (B – 80 – 89)
Linares
High Shooter (100)

## Slide 23: Questions / Comments

## Slide 24
Chapter 8 – Flight Manuals
FAA – Pilot’s Handbook of Aeronautical Knowledge

## Slide 25: Today’s Mission Requirements
Mission:
Describe in writing how AFM/POH and documents such as ADs help a pilot to have ready access to pertinent information needed to safely fly a particular aircraft.
Describe what information can be found in the AFM/POH to help a pilot make good flight decisions.
Identify what preventive maintenance is allowed on the aircraft, and how a pilot can maintain his or her aircraft in an airworthy condition.
Describe why flight manuals and aircraft documentation are essential tools used to reach the goal of safe flight.
EQ:
  Describe the importance of Aeronautical Knowledge for the student pilot learning to fly.

## Slide 26: Introduction
This chapter covers airplane flight manuals (AFM), the pilot’s operating handbook (POH), and aircraft documents pertaining to ownership, airworthiness, maintenance, and operations with inoperative equipment.

## Slide 27: Introduction
Knowledge of these required documents and manuals is essential for a pilot to conduct a safe flight.

## Slide 28: Pilots Operating Handbook
The POH is a document developed by the aircraft manufacturer and contains FAA approved Airplane Flight Manuals (AFM) information.
The POH for most light aircraft built after 1975 is also designated as the FAA-approved flight manual.

## Slide 29: Pilots Operating Handbook / Airplane Flight Manual
The typical AFM/POH contains the following nine sections:
  General;
  Limitations;
  Emergency Procedures;
  Normal Procedures;
  Performance;
  Weight and Balance/Equipment List;
  Systems Description;
  Handling, Service, and Maintenance;
  Supplements.

## Slide 30: Aircraft Documents
Certificate of Aircraft Registration
Before an aircraft can be flown legally, it must be registered with the FAA Aircraft Registry.
The Certificate of Aircraft Registration, which is issued to the owner as evidence of the registration, must be carried in the aircraft at all times.

## Slide 31: Airworthiness Certificate
An Airworthiness Certificate is issued by a representative of the FAA after the aircraft has been inspected, is found to meet the requirements of 14 CFR part 21, and is in condition for safe operation.

## Slide 32: Airworthiness Certificate
The Airworthiness Certificate must be displayed in the aircraft so it is legible to the passengers and crew whenever it is operated.
The Airworthiness Certificate is transferred with the aircraft except when it is sold to a foreign purchaser.

## Slide 33: Airworthiness Inspections
14 CFR part 91, subpart E, requires the inspection of all civil aircraft at specific intervals to determine the overall condition.
The interval depends upon the type of operations in which the aircraft is engaged.

## Slide 34: Airworthiness Inspections
All aircraft need to be inspected at least once each 12 calendar months, while inspection is required for others after each 100 hours of operation.

## Slide 35: Minimum Equipment Lists (MEL)
14 CFR requires that all aircraft instruments and installed equipment be operative prior to each departure.

## Slide 36: Minimum Equipment Lists (MEL)
When the FAA adopted the minimum equipment list (MEL) concept for 14 CFR part 91 operations, this allowed operations with inoperative equipment determined to be nonessential for safe flight.

## Slide 37: Maintenance Entries
All pilots who maintain or perform preventive maintenance must make an entry in the maintenance record of the aircraft.

## Slide 38: Maintenance Entries
The entry must include:
  1. A description of the work, such as “changed oil (Shell Aero-50) at 2,345 hours.”
  2. The date of completion of the work performed.
  3. The entry of the pilot’s name, signature, certificate number, and type of certificate held.

## Slide 39: Aircraft Owner/Operator Responsibilities
The registered owner/operator of an aircraft is responsible for:
  Having a current Airworthiness Certificate
  Certificate of Aircraft Registration in the aircraft.

## Slide 40: Aircraft Owner/Operator Responsibilities
Maintaining the aircraft in an airworthy condition, including compliance with all applicable ADs, and assuring that maintenance is properly recorded.
Keeping abreast of current regulations concerning the operation and maintenance of the aircraft.

## Slide 41: Chapter Summary
The goal of every pilot is a safe flight; flight manuals and aircraft documentation are essential tools used to reach that goal.

## Slide 42: Questions / Comments

## Slide 43: 2nd Quarter Requirements (9 weeks – May 18)
All students will complete the following:
  Take notes - All in class quizzes and tests
  Private Pilot Syllabus
    Lessons 1 – 5 (Taxiing through Air Traffic Control)
    Must pass written with 80%
    Successfully complete 3 times on small sim
    Successfully complete 1 time on Main sim
  Complete ERAU Aviation 101
    3 quizzes and 1 test
  Student will receive zero points for all incomplete work – NO make-up / extra credit
NOTE: All unfinished Student Pilot and ERAU must be complete prior to starting Private Pilot and last 3 quizzes and test for ERAU.