## Slide 1: Warm-Up – 3/29 – 10 minutes
Utilizing your notes and past knowledge answer the following questions:
What is a major concern with water on runways with respect to aircraft operation?
What is the concern if an aircraft lands at higher speed when a runway is wet?
What is the norm for takeoff speeds of an aircraft?
Describe the three concerns with a heavy aircraft during takeoff.
What is required if there is an increase in weight in order for an aircraft to takeoff?

## Slide 2: Questions / Comments

## Slide 3: Warm-Up – 3/29 – 10 minutes
Utilizing your notes and past knowledge answer the following questions:
What is a major concern with water on runways with respect to aircraft operation?
What is the concern if an aircraft lands at higher speed when a runway is wet?
What is the norm for takeoff speeds of an aircraft?
Describe the three concerns with a heavy aircraft during takeoff.
What is required if there is an increase in weight in order for an aircraft to takeoff?

## Slide 4: Water on the Runway and Dynamic Hydroplaning
Water on the runways reduces the friction between the tires and the ground, and can reduce braking effectiveness.
This is also true of braking effectiveness when runways are covered in ice.

## Slide 5: Warm-Up – 3/29 – 10 minutes
Utilizing your notes and past knowledge answer the following questions:
What is a major concern with water on runways with respect to aircraft operation?
What is the concern if an aircraft lands at higher speed when a runway is wet?
What is the norm for takeoff speeds of an aircraft?
Describe the three concerns with a heavy aircraft during takeoff.
What is required if there is an increase in weight in order for an aircraft to takeoff?

## Slide 6: Water on the Runway and Dynamic Hydroplaning
Landing at higher than recommended touchdown speeds will expose the aircraft to a greater potential for hydroplaning.
And once hydroplaning starts, it can continue well below the minimum initial hydroplaning speed.

## Slide 7: Warm-Up – 3/29 – 10 minutes
Utilizing your notes and past knowledge answer the following questions:
What is a major concern with water on runways with respect to aircraft operation?
What is the concern if an aircraft lands at higher speed when a runway is wet?
What is the norm for takeoff speeds of an aircraft?
Describe the three concerns with a heavy aircraft during takeoff.
What is required if there is an increase in weight in order for an aircraft to takeoff?

## Slide 8: Takeoff Performance
Depending on the aircraft characteristics, the lift-off speed will be anywhere from 1.05 to 1.25 times the stall speed or minimum control speed.

## Slide 9: Warm-Up – 3/29 – 10 minutes
Utilizing your notes and past knowledge answer the following questions:
What is a major concern with water on runways with respect to aircraft operation?
What is the concern if an aircraft lands at higher speed when a runway is wet?
What is the norm for takeoff speeds of an aircraft?
Describe the three concerns with a heavy aircraft during takeoff.
What is required if there is an increase in weight in order for an aircraft to takeoff?

## Slide 10: Takeoff Performance
1. Higher lift-off speed
2. Greater mass to accelerate
3. Increased retarding force (drag and ground friction)

## Slide 11: Warm-Up – 3/29 – 10 minutes
Utilizing your notes and past knowledge answer the following questions:
What is a major concern with water on runways with respect to aircraft operation?
What is the concern if an aircraft lands at higher speed when a runway is wet?
What is the norm for takeoff speeds of an aircraft?
Describe the three concerns with a heavy aircraft during takeoff.
What is required if there is an increase in weight in order for an aircraft to takeoff?

## Slide 12: Takeoff Performance
If the gross weight increases, a greater speed is necessary to produce the greater lift necessary to get the aircraft airborne.

## Slide 13: Questions / Comments

## Slide 14: THIS DAY IN AVIATION
March 29
1858 — Two men, Brown and Dean, make the first balloon flight in Australia in a hydrogen balloon named the “Australasian.”

## Slide 15: THIS DAY IN AVIATION
March 29
1920 — Located about 10 miles due south of the City of London, England, Waddon Airport at Croydon is used for the first time as London's airport.
Until this date, Hownslow has been considered the capital's main airport.

## Slide 16: THIS DAY IN AVIATION
March 29
1923 — Lieut. Alexander Pearson, USAS, makes a record 500 km flight, 167.8 mph in a Verville-Sperry, with Wright 350-hp engine, at McCook Field, Dayton, Ohio.

## Slide 17: THIS DAY IN AVIATION
March 29
1923 — Lieut. L. J. Maitland, USAS, at McCook Field, makes a record speed flight in an Army-Curtiss Racer, 239.95 mph.

## Slide 18: THIS DAY IN AVIATION
March 29
1923 — Lieut. H. R. Harris, USAS, in a DH-4B at Dayton, Ohio, establishes a world record for 1,000 km of 127.4 mph.
Harris also sets record of 114.35 mph for 1,500 km.

## Slide 19: THIS DAY IN AVIATION
March 29
1951 — Flight Safety Inc. begins operations at the Marine Air Terminal at LaGuardia Airport, New York with just one secretary and rented late night hours on a Link trainer simulator.

## Slide 20: Questions / Comments

## Slide 21
Sunday | Monday | Tuesday | Wednesday | Thursday | Friday | Saturday
26 | 27 Chapter 10 Aircraft Performance | 28 Chapter 10 Aircraft Performance | 29 Chapter 10 Aircraft Performance | 30 Chap 10 Test | 31 Flight Line Friday | 1
2 | 3 Chapter 11 Weather Theory | 4 Chapter 11 Weather Theory | 5 Chapter 11 Weather Theory | 6 SCHOOL VISIT | 7 Flight Line Friday Chap 11 Test | 8
9 | 10 SCHOOL VACATION | 11 SCHOOL VACATION | 12 SCHOOL VACATION | 13 SCHOOL VACATION | 14 SCHOOL VACATION | 15
16 | 17 Chapter 12 Weather Services | 18 Chapter 12 Weather Services | 19 Chapter 12 Weather Services | 20 Chapter 12 Weather Services Review and Test | 21 Flight Line Friday | 22
March / April 2017

## Slide 22: 2nd Quarter Requirements (8 weeks – May 24)
All students will complete the following:
  Take notes - All in class quizzes and tests
  Private Pilot Syllabus
    Lessons 1 – 5 (Taxiing through Air Traffic Control)
    Must pass written with 80%
    Successfully complete 3 times on small sim
    Successfully complete 1 time on Main sim
  Complete ERAU Aviation 101
    3 quizzes and 1 test
  Student will receive zero points for all incomplete work – NO make-up / extra credit
NOTE: All unfinished Student Pilot and ERAU must be complete prior to starting Private Pilot and last 3 quizzes and test for ERAU.

## Slide 23: Questions / Comments

## Slide 24
Chapter 10 – Aircraft Performance
FAA – Pilot’s Handbook of Aeronautical Knowledge

## Slide 25: Today’s Mission Requirements
Mission:
Describe the factors that affect aircraft performance.
Identify how aircraft weight, atmospheric conditions, runway environment, and the fundamental physical laws governing the forces can affect aircraft performance.
EQ:
  Describe the importance of Aeronautical Knowledge for the student pilot learning to fly.

## Slide 26: Takeoff Performance
The effect of wind on takeoff distance is large.
The effect of a headwind is to allow the aircraft to reach the lift-off speed at a lower groundspeed while the effect of a tailwind is to require the aircraft to achieve a greater groundspeed to attain the lift-off speed.

## Slide 27: Takeoff Performance
The effect of proper takeoff speed is especially important when runway lengths and takeoff distances are critical.
The takeoff speeds specified in the AFM/POH are generally the minimum safe speeds at which the aircraft can become airborne.

## Slide 28: Takeoff Performance
Any attempt to take off below the recommended speed means that the aircraft could stall, be difficult to control, or have a very low initial rate of climb.

## Slide 29: Takeoff Performance
Excessive airspeed at takeoff may improve the initial rate of climb and “feel” of the aircraft, but will produce an undesirable increase in takeoff distance.

## Slide 30: Landing Performance
The effect of gross weight on landing distance is one of the principal items determining the landing distance.

## Slide 31: Landing Performance
One effect of an increased gross weight is that a greater speed will be required to support the aircraft at the landing AOA and lift coefficient.

## Slide 32: Landing Performance
The landing speeds specified in the AFM/POH are generally the minimum safe speeds at which the aircraft can be landed.

## Slide 33: Landing Performance
Any attempt to land at below the specified speed may mean that the aircraft may stall, be difficult to control, or develop high rates of descent.

## Slide 34: Landing Performance
An excessive speed at landing may improve the controllability slightly (especially in crosswinds), but causes an undesirable increase in landing distance.

## Slide 35: Landing Performance
The most critical conditions of landing performance are combinations of high gross weight, high density altitude, and unfavorable wind.

## Slide 36: Questions / Comments

## Slide 37: 2nd Quarter Requirements (8 weeks – May 24)
All students will complete the following:
  Take notes - All in class quizzes and tests
  Private Pilot Syllabus
    Lessons 1 – 5 (Taxiing through Air Traffic Control)
    Must pass written with 80%
    Successfully complete 3 times on small sim
    Successfully complete 1 time on Main sim
  Complete ERAU Aviation 101
    3 quizzes and 1 test
  Student will receive zero points for all incomplete work – NO make-up / extra credit
NOTE: All unfinished Student Pilot and ERAU must be complete prior to starting Private Pilot and last 3 quizzes and test for ERAU.