## Slide 1: MGMT 203 Airports, Airspace, and Air Traffic Control Management
Module 7

## Slide 2: THIS DAY IN AVIATION
November 14
1910 — The birth of the aircraft carrier occurs when Eugene Ely takes off from the cruiser USS Birmingham in Virginia, on a Curtiss biplane.
The warship has an 83-foot platform built over the foredeck for the take-off.

## Slide 3: THIS DAY IN AVIATION
November 14
1949 — Boeing Airplane Company begins delivery to the United States Air Force of B-50D's equipped with droppable fuel tanks.

## Slide 4: THIS DAY IN AVIATION
November 14
1957 — Chance Vought “Regulus II” completes successful rocket-boosted flight test by United States Navy.

## Slide 5: THIS DAY IN AVIATION
November 14
1966 — A Lockheed C-141 “Starlifter” became the first jet aircraft to land in Antarctica.

## Slide 6: Questions / Comments

## Slide 7: Learning Objectives – Module 7 (11/13/17 – 11/21/17) Airports, Airspace, and Air Traffic Control Management
Upon successful completion of this module, you will be able to:
Explain the impact of airport design, development, operations, and funding sources on airport systems.
Explain the purpose of an airport.
Describe Air Traffic Control Towers (ATCTs) and their purpose.
Compare air traffic control systems between en route, terminal, tower, and flight service functions.
Demonstrate an understanding of the Title 14 CFR Parts that are used to operate airports.
Explain the purpose of the Air Traffic System Command Center (ATCSCC) and location.
Outline the basic structure of the national airspace system, and describe the impact of the FAA's National Airspace System Plan (NASP).
Describe the Flight Service Station (FSS) and its services.
Describe the requirements for a reliever airport classification.
Critique the Airport Certification Manual.
Describe the Airport Emergency Plan (AEP) requirements.
Management of Aeronautical Science
Mon/Tues/Wed

## Slide 8: Readings
Refer to Readings on ERAU Website Mod 7
Pilots Handbook of Aeronautical Knowledge
  Chapter 14 – Airport Operations
  Chapter 15 – Airspace
Title 14 Code of Federal Regulations (CFR) - Please review 14 CFR Parts:
  36, 71, 73, 139, and 150.
Textbook – Business and Corporate Aviation Management
  Chapter 5: Flight Department

## Slide 9
SUNDAY | MONDAY | TUESDAY | WEDNESDAY | THURSDAY | FRIDAY | SATURDAY
5 | 6 Module 6 Human Factors and CRM | 7 Module 6 Human Factors and CRM | 8 Module 6 Human Factors and CRM Discussion Due | 9 Module 6 Human Factors and CRM | 10 Flightline Friday Review Questions Due | 11
12 | 13 Module 7 Intro Airports, Airspace, and Air Traffic Control Management | 14 Module 7 Airports, Airspace, and Air Traffic Control Management | 15 Module 7 Airports, Airspace, and Air Traffic Control Management | 16 Beaufort County Airport (ILT) | 17 Flightline Friday | 18
19 | 20 Module 7 Airports, Airspace, and Air Traffic Control Management Discussion Due | 21 Module 7 Airports, Airspace, and Air Traffic Control Management Review Questions Due | 22 NO SCHOOL | 23 NO SCHOOL Thanksgiving | 24 NO SCHOOL | 25
November 2017

## Slide 10: 7.2 – Discussion: Problems and Difficulties with Air Travel Mon Nov 20

## Slide 11: 7.4 – Discussion: Video Analysis: FAA Gate to Gate – NextGen Explained Mon Nov 20

## Slide 12: Module 7 Review Questions (Due Tues Nov 21)
Spend quality time responding to the following questions in your own words.
Explain the purpose of an airport.
Describe Air Traffic Control Towers (ATCTs) and their purpose.
Demonstrate an understanding of the Title 14 CFR Parts that are used to operate airports. Please state at least five parts we discussed in the course.
Describe the Flight Service Station (FSS) and the services it can provide.
Describe the requirements for a reliever airport classification.

## Slide 13: Term Paper Topics
Aircraft Manufacturing Management
- Chris Corbett
Fire and Crash Rescue Management
- Trent Thompson
Helicopter Operations Management
- Casey Bradford
Your Final Term Paper must be at least 12 pages and consist of the following:
A title page
Main text (10 pages)
Reference page (current APA format)
The paper should include some of the headings below as appropriate:
Introduction
Description of the Company or Agency (Basically what business are you in)
Operation Description
Equipment or Aircraft
Maintenance Requirements
Manager’s Roles and Responsibilities
Staff Qualifications, Certifications, and Responsibilities
Human Factors
Quality Requirements
Regulations and Laws
Safety
Security
Environmental Responsibilities
Other Management Factors Considered
References (current APA format)
DUE Friday Dec 8, 2017

## Slide 14: Assignments Due – Module 7 (11/13/17 – 11/21/17)
Review Module 7 Instructions for the following assignments:
Discussion Board Due (Problems with Air Travel)
  (Due – Mon Nov 20) – 2 part (Post and Respond)
Discussion Board Due (Video Analysis)
  (Due – Mon Nov 20) – 2 part (Post and Respond)
Review Questions – Airports, Airspace and ATC
  (Due – Tues Nov 21) – 5 Questions
Management of Aeronautical Science

## Slide 15: Questions / Comments

## Slide 16: Airports

## Slide 17: Airport Markings
Used for control and communications
Ground markings and lights
  Runway markings
    Painted white and white lights at night
  Taxiway markings
    Painted yellow
    Blue lights
  Vehicle roadway markings
  Boundary markings for non-movement areas
Have many types of lights that are dependent upon airport complexity but are standardized.

## Slide 18: Airport Markings
FAA. (2008). FAA-H-8083-25
Pilot's Handbook of Aeronautical Knowledge.
p. 13-5

## Slide 19: Airport Signs
Used for control and communication
Complexity of airport determines the amount of signs for communication.
Types
  Mandatory instruction signs
    Runway, critical area, or prohibited area
    Example is white letters on red background
      Runway holding position
  · Location signs
    Taxiway or runway location
  Direction signs
    Black letters on yellow background = Provide directions

## Slide 20: Airport Signs
Types
      Destination signs
    Yellow background with black letters and arrows
    Terminal
    Parking area
    Cargo terminal
  Information signs
    Yellow background with black letters
    Frequencies and noise abatement requirements
  Runway distance remaining signs
    Black background with white numbers indicating thousands of feet
(FAA, pp. 13-4 - 13-6, 2008)

## Slide 21: Airport Signs
FAA. (2008). FAA-H-8083-25 Pilot's Handbook of Aeronautical Knowledge. p. 13-6

## Slide 22: Aircraft Rescue and Firefighting (ARFF)
Crash, Fire, and Rescue (CFR)
  FAA changed from CFR to ARFF in 14 CFR Part 139
Different equipment and apparatus
  ARFF Vehicles
  Hoses and Nozzles
  Accessories
  Personal Protective Equipment (PPE)
  Extinguishing agents
    Water
    Foam
    Dry Chemicals
  Rescue tools and equipment

## Slide 23: Aircraft Rescue and Firefighting (ARFF)
14 CFR Part 139 designates the airport ARFF index
  The length of aircraft from nose to tail that depart the airport on an average of five departures per day.
  Determine the type and number of ARFF equipment required.
ARFF index
  A: Aircraft less that 90 feet in length
  B: Aircraft more than 90 feet but less than 126 feet in length
  C: Aircraft more than 126 feet but less than 159 feet in length
  D: Aircraft more than 159 feet but less than 200 feet in length
  E: Aircraft greater than 200 feet in length

## Slide 24: Noise Abatement and Control
Title 14 CFR Part 150 Noise Control Compatibility Planning Program.
AC 150/5020-1 Noise Control and Compatibility Planning for Air­ports.
Title 14 CFR Part 36 Noise Standards: Aircraft Type and Airworthiness.
  Airport neighbors noise complaints are common especially during 11 pm to 7 am timeframe.
    This can be a constraint for maintenance
Airport may have procedures in place to climb as soon as possible to prevent excessive noise.

## Slide 25: Bird and Wildlife Hazard Management
Birds and other wildlife strikes are common in the vicinity of airport.
  There have been reports that indicate aircraft damage and in some cases loss of life.
14 CFR Part 139 requires airport operators to have policies and procedures for identification, correction and control, and prevention of these hazards.

## Slide 26: ICAO Airport
U.S. airports serving international operations
Article 68 of the Convention on International Civil Aviation.
AC 150/5000-16 Lists all U.S. international airports, designated airports.
Airports served by scheduled and nonscheduled international air transport and international general aviation flights.

## Slide 27: Airport Safety Self-Inspection
Title 14 CFR Part 139 Certification of Airports
AC 150/5200-18B
Responsibility of the airport owner or operator.
Used to prevent injury and aircraft/ airport damage.
Multiple inspection frequencies.
Inspection results must be documented and kept
  Follow up and feedback are necessary

## Slide 28: Management Perspective
Communicate, communicate, and communicate.
Know the airport rules and regulations.
Understand the meaning of signs, lights, and and markings.
Situational awareness in a must for safe operations.
Vehicle Control Plan is necessary for safe operations especially on the air-side of the airport.

## Slide 29: Vehicle Control
FAA. (2008). FAA-H-8083-25 Pilot's Handbook of Aeronautical Knowledge. p. 13-5

## Slide 30: Questions / Comments

## Slide 31: Air Traffic Control

## Slide 32: Air Traffic Control (ATC)
Promote the safe, orderly, and expeditious flow of air traffic.
Determined by controlled airspace classification
  Will discuss classes in airspace slides.

## Slide 33: Air Traffic Control System
Operated by FAA
Includes
  Majority of air traf­fic control towers
  Visual and electronic navigational aids
    At and near airports
  Rules and procedures that govern civil aviation and airport operations.
  Provides airport improve­ment and expansion funding.

## Slide 34: Air Traffic Control System Command Center (ATCSCC)
Top level of Air Traffic Control System
Manages air traffic and every aircraft within the continental United States.
Balances demand with system capacity within the National Airspace System (NAS).
  Maximizes overall operation
Authority to declare ground holds to avoid congestion.
Currently located in Warrenton, VA

## Slide 35: Air Route Traffic Control Centers (ARTCCs)
Monitor enroute aircraft and aircraft in high-altitude cruise.

## Slide 36: Terminal Radar Approach Control (TRACON) Facilities
Regional air traffic control centers.
Control the movement of air traffic in altitudes un­der 18,000 Mean Sea Level (MSL).
Controller hands over a landing aircraft within 5 miles of an airport and below 2,500 feet to airport terminal air traffic controllers.

## Slide 37: Air Traffic Control Towers (ATCTs)
Terminal facility.
Provide services to aircraft operating in the vicinity of an airport or on movement area.
Authorizes aircraft to land or takeoff or to transit the Class D airspace area.
May provide approach control services.
Majority of towers are managed by FAA.
Some are contract managed with restrictions.

## Slide 38: Flight Service Station (FSS)
Air traffic facility
Provide many services
  Pilot briefing
  Assistance in emergency situations
  Provide Notices to Airmen (NOTAM)
  Weather information and observations
  Receive and process Instrument Flight Rules (IFR) flight plans
  Monitor NAVAIDs
  Airport advisories

## Slide 39: Other ATC Facilities
Automated Flight Service Stations (AFSS)
  Subcontracted to the Lockheed Martin Flight Services
    FAA oversight
  Provides information and services to pilots
  Communicate clearances from ATC as required
  Do not give ATC instructions, clearances, or separation
Ground Control
  Control aircraft during taxi to and from runways.
  May have Surface Movement Radar (SMR) to monitor aircraft and vehicles movement on the ground.
  Automated Flight Service.

## Slide 40: Flight Plan
Provides aircraft intended flight information
Filed with Flight Service Station or an Air Traffic Control facility
  Orally or written
  Receive and process Instrument Flight Rules (IFR) flight plans
    Also special Visual Flight Rule (VFR) procedures
  May file, activate, close, or change a flight plan

## Slide 41: Flight Plan
FAA. (2008). FAA-H-8083-25 Pilot's Handbook of Aeronautical Knowledge. p. 15-21

## Slide 42: Airspace

## Slide 43: Controlled Airspace
Airspace where aircraft may be sub­ject to air traffic control
  Considered boundaries above earth’s surface or a specific portion if airspace
There are different classes of controlled airspace
14 CFR Part 71 Designation of Class A, B, C, D, and E Airspace Areas; Air Traffic Routes; and Reporting Requirements.

## Slide 44: Controlled Airspace
FAA. (2008). Pilot's Handbook of Aeronautical Knowledge, p. 14-2

## Slide 45: Controlled Airspace
Class A Airspace
  Positive control airspace
  Airspace located throughout the United States beginning at an altitude of 18,000 feet Mean Sea Level (MSL) up to 60,000 MSL.
  Conducted under IFR

## Slide 46: Controlled Airspace
Class B Airspace
  Terminal radar service areas.
  Airspace surrounding the nation's busiest airports.
  Must have ATC clearance to operate in the area.

## Slide 47: Controlled Airspace
Class C Airspace
  Airport radar service areas.
  Airspace surrounding airports of moderately high levels of IFR operations or passenger enplanements.
  Must establish two-way radio communications with the ATC facility prior to entering the airspace and maintain that communication in the airspace.

## Slide 48: Controlled Airspace
Class D Airspace
  Control zones
  Airspace surrounding those airports not in Class B or Class C airspace but do have an air traffic control tower in op­eration.
    Must establish two-way radio communications with the ATC facility prior to entering the airspace and maintain that communication in the airspace.

## Slide 49: Controlled Airspace
Class E airspace
  General controlled airspace
  Airspace that generally ex­ists in the absence of Class A, B, C, or D airspace extending from the sur­face to 18,000 feet MSL within 5 miles or airports without control towers but with instrument approach procedures.

## Slide 50: Controlled Airspace
Class G airspace
  Uncontrolled airspace
  Airspace in the absence of Class A, B, C, D, or E airspace
  Maintain visual flight rules (VFR) minimums

## Slide 51: Class Airspace
FAA. (2008). Pilot's Handbook of Aeronautical Knowledge, p. 14-9

## Slide 52: Special Use Airspace
Prohibited areas (White House)
Restricted areas (artillery fire)
Military operations areas (MOA)
Alert areas (high volume pilot training)
Warning areas (hazardous flight activity)
Controlled firings areas (rocket firing)
Title 14 CFR Part 73—Special Use Airspace provides information on restricted and prohibited areas

## Slide 53: Temporary Flight Restrictions (TFR)
Airspace areas restricted for a specific period of time
TFR issued for
  National security
    9/11
    Potential terrorist activity
  Military operations
  Hazards or disasters
  Accidents
  Space launch and recovery operations

## Slide 54: Notice to Airmen (NOTAM)
Contains information identifying any condition or change in any facility, service, hazards, or procedures with flight operations.
Reductions in capability.
Another notification is the Airport/Facility Directory.
Title 14 CFR Part 139 Certification of Airports.

## Slide 55: Notice to Airmen (NOTAM)
FAA. (2008). FAA-H-8083-25 Pilot's
Handbook of Aeronautical
Knowledge. p. 1-12

## Slide 56: National Airspace System (NAS)
Consists of organization of airports, facilities, airspace, and air traffic control.
  Integration of equipment, processes and procedures, and systems.
Provides a safe and systematic flying environment.
Consist of United States civil aviation system.
Consider the classes of controlled airspace.

## Slide 57: National Airspace System Plan (NASP)
Specifies development projects required to improve public airports to meet the demands of civil aviation.
Includes strategic goals for NAS
Specifies NAS modernization
  Communication
  Navigation
  Surveillance
  Weather Automation Systems
  Avionics
  Operations
  Free Flight (NextGen)

## Slide 58: Free Flight (NextGen)
ATC and National Airspace System (NAS) modernization.
Global Positioning System (GPS) navigation that allows direct routes between airports.
ATC controllers monitor and perform surveillance
Consists of
  Aeronautical data link systems communication
    Controller-to-pilot data link
  GPS navigation system
  Traffic Alert and Collision Avoidance System (TCAS)
  Automated Dependent Surveillance (ADS)
  Weather
    Integrated Terminal Weather System (ITWS)
    Weather and Radar Processor
  Enroute enhancements

## Slide 59: NAS Capital Investment Plan (CIP)
Appendix B For Fiscal Years 2014 to 2018.
Provides metrics (measures) to link to Department of Transportation and Federal Aviation Administration strategic plans.
Contains budget line items for specific programs and schedules.
  Next Generation Air Transportation System (NextGen)
  Runway Incursion Reduction Program, etc.

## Slide 60: Questions / Comments